## Slide 1: Perforating Requirements for Fracture Stimulation
Andy Martin, Larry Behrmann, Brenden Grove, Harvey Williams, Gerardo Arguello
Presented by:
Frank Thompson
Business Development Mgr North Europe

## Slide 2: Agenda
Perforating objectives for fracture stimulation
Effect of perforating parameters
Horizontal wells
Conclusions

## Slide 3: Perforating Objectives for Fracturing
Make frac jobs more effective
  Lower breakdown pressures
  Lower treatment pressures with better treatment rates
  Controlled frac placement
All of this leads to better production
Also helps avoid disasters like aborted jobs

## Slide 4: Perforating Objectives
Perforations should minimize:
  Near wellbore pressure drop
  Perforation friction
  Tortuosity
  Micro-annulus pinch points
  Multiple competing fractures

## Slide 5: What can we control?
  Size and type of gun
  Penetration (type of charge)
  Casing entrance hole
  Shot density
  Shot phasing
  Interval length
  Gun orientation

## Slide 6: Casing Entrance Hole
EH size about 8 to 10 times proppant diameter to prevent bridging
Consistent EH for accurate limited entry designs
40% variation in EH results in 120% increase in pressure drop
(from SPE 83590)
Chart: EH variation vs Error in Pressure Calculation
| 0 | 1.6686518214146266E-3 | 6.6985168428592675E-3 | 1.5161986112006039E-2 | 2.7181948390295103E-2 | 4.2935249345083873E-2 | 6.2657748525066115E-2 | 8.6651204611403645E-2 | 0.11529231029548553 | 0.14904431073199195 | 0.18847178242392501 | 0.23425933409042299 | 0.28723523318979927 | 0.34840128293482137 | 0.41897070506629658 | 0.500416366046882 | 0.59453247965051659 | 0.70351401503499345 | 0.83005956432089445 | 0.97750556597791849 | 1.1500028206750725
 | 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4
EH variation
Error in pressure

## Slide 7: Minimizing Casing Entrance Hole Variation
  Use largest gun possible to reduce water clearance
  Centralize gun
  Design shaped charge for minimum variation even across large water clearances
Std
Frac charge
New Frac charge
Best Frac Charge

## Slide 8: Is Penetration Important ?
Sometimes ignored (we just need some holes in the casing)
What about near wellbore conditions?
  breakouts
  formation damage?
  near wellbore stress?
Frac experts starting to realize that penetration is a benefit (>1 BH)
Connection to the far field helps avoid near-wellbore tortuosity effects
Up to 5-inch damage (SPE 112862)

## Slide 9: What about Clean Perforations?
Enable injection to start deeper in formation, avoids near wellbore damaged zone
Fractures may not initiate from plugged perforations (see “big block” tests left)
Clean perforations allow fluid leak-off, increasing near-wellbore pressure prior to fracture initiation
(from SPE 143997)
Plugged perforations NO fracture
Clean Perforations with fracture passing through perforations
(from SPE 20661)

## Slide 10
Plugged perfs  NO fracture
(from SPE 20661)

## Slide 11
Clean Perfs  Fracture
(from SPE 20661)

## Slide 12: Gun Phasing and Direction Near-vertical wells
Fractures initiate from perforations aligned with maximum stress direction
Best gun phasing is 0° – 180° in max stress direction
Perforations aligned with maximum horizontal stress
(from SPE 20661)

## Slide 13
Perforations aligned with maximum horizontal stress
(from SPE 20661)

## Slide 14: Gun Phasing and Direction Near-vertical wells
Fractures initiate from sand-face when perforations are misaligned
Other gun phasings: 120° (at 1 ½ times spf); 60° (at 3 times spf)
Perforations misaligned with maximum horizontal stress
(from SPE 20661)

## Slide 15
Perforations not aligned with maximum horizontal stress
(from SPE 20661)

## Slide 16: Well Direction and Gun Phasing
Gun phasing and interval perforated should be based on well direction compared to the preferred fracture plane

## Slide 17: Hydraulic Fractures in Horizontal Wells
What we want
Transverse fracs
Longitudinal fracs

## Slide 18: What We Get with 60° Phasing
Longitudinal fractures initiate first Terminate about 2 wellbore diameters in vertical direction
  Extend along wellbore
  Initial pumped volumes dominated by longitudinal fracs
Transverse fractures initiate after
  Perpendicular to longitudinal
  Do not rotate from longitudinal

## Slide 19
What we get
with
60° Phasing

## Slide 20: Can We Do Better?
Several experiments done in large blocks in a tri-axial stress frame to simulate horizontal well
Both DP and BH charges used
Directional perforations aimed at the same transverse plane
Transverse fracture from directed perforations
Result: Transverse fractures created

## Slide 21
Directional perforations in the same transverse plane
transverse fractures are created

## Slide 22: Perforation Gun Length-Horizontal Wells
In horizontal wells perforation length should be limited to about 2 to 4 times the wellbore diameter (ref SPE 19720)
  Minimizes multiple competing fractures
Typical gun contains 6 to 10 shots (60° phased)
2 to 4 guns are shot for each frac stage
Guns run with addressable switches in pumpdown plug-n-perf mode

## Slide 23: How Many Clusters per Stage?
Closely spaced clusters increases flow rate in gas shales
  Trade off is cost (number of fractures vs production)
  SPE 144326 shows study on production vs clusters for major shale plays
Reducing the number of clusters increases odds of all clusters being stimulated
  48% of perf clusters aren’t contributing in wells having 6 or more perf clusters / frac stage
Cluster placement should be matched to reservoir quality
  Requires detailed modeling
  SPE 146872 and SPE 146876 detail modeling work flow

## Slide 24: Horizontal shale well production log analysis

## Slide 25: Conclusion Well planned perforating will make frac jobs more effective
Careful choice of shaped charges, gun phasing and orientation will help initiate fractures and minimize tortuosity
In horizontal wells selection of number of shots, position of clusters impacts well productivity

## Slide 26: Questions?