## Slide 1: 2015 International Perforating Symposium The Renaissance Hotel, Amsterdam 19th -21st May 2015
Ultra high pressure gun system developed for Gulf of Mexico
Charlie McClean, Parry Hillis, Didhiti Talipatra
IPS – 15 - 23

## Slide 2
Agenda
Introduction
Perforating System Requirements
  Steel
  Gun System
  Firing System
  Explosives
Individual Component Testing and Certification
System Qualification
SIT
Quality Plan
Conclusion

## Slide 3: Introduction
Perforating is a critical step in establishing connectivity between subsurface zones and the wellbore in a well where the casing is cemented across the proposed production zone.
Over the past few years the need to drill wells with increasingly higher pressures and temperatures has increased and will continue to grow.
Steel strip to hold shaped charges in place
Shaped charges
  Case
  Liner
  Main charge load
  Primer load
Detonating cord that connects to the back of each shaped charge
Boosters crimped to each end of the detonating cord
Hollow carrier into which the assembly fits
Connecting sub (tandem)
Baker Standard Gun System BSGS

## Slide 4: Perforating System Requirements
What did we want to deliver in the 35,000 psi TCP system?
A system that would withstand Ultra HPHT firing pressures.
Limited post detonation gun swell.
Limited wall thickness.
Fully redundant firing system.
Ultra deep penetrating (Hard Rock shaped charge).
Conveyance flexibility.
Reliability.
High level of service quality.
Risk reduction through up-front modeling
Notes: BHI did not want to just increase the gun wall thickness as this would effect the available charge size and performance through the gun wall.
Convenience of flexibility to run TCP or WL

## Slide 5: Steel
During the past few years, technology has greatly improved the capabilities of “high-strength, low-alloy steel”
Critical elements of both steel selection and deliver.
Focus on more than yield strength.
Work with several testing providers.
Incorporate a test program in to the quality plan
Work closely with all vendors.
Any detected anomaly in the material specification must be identified as early in the process as possible so that corrective action can be implemented and another run of the material can be produced.
Notes: The steel had to be nothing less than perfect with no variation in the specification. The steel vendors worked side by side with BHI during the quality plan.

## Slide 6: Gun System
The gun system had to meet the following criteria:
Include the conventional tandem sub connector.
Pass all specification tests before and after machining.
Post detonation survivability.
Capable of housing a fit for purpose shaped charge.
Maintain a safety factor.
The applied pressure with the maximum principal stress of 137,130 psi at 470°F
Gun body after ballistic survival shot test
Notes: Include the conventional tandem sub connector rather than a new design.
The material was tested before and after the material was machined to ensure high level of service quality was maintained.
Post detonation survivability was critical in the UHPHT environment to ensure safe recovery
Capable of housing a fit for purpose shaped charge to maximize performance from the HNS charge
Maintain a safety factor to again insure safe recovery

## Slide 7: Firing System
Firing system requirements:
Not mechanical.
Fully redundant.
Rupture disc activated.
Incorporate a time delay.
Reliable.
Simplistic in function.
Surface Safe.
Tested in accordance with API RP-67.
Ultra HPHT Model D, RD Firing System
Notes: Not mechanical.
Fully redundant as with any HPHT project as a minimum
Rupture disc activated rather than shear pins for better accuracy
Incorporate a time delay to allow for the firing pressure to be bled down
Reliable, so we used one of our most reliable systems with thousands of successful runs. And modified the components to handle these extreme conditions.
Simplistic in function.
Surface Safe and incorporate all aspects of our conventional surface safe firing systems
Tested in accordance with API RP-67.

## Slide 8: Explosives
The high-temperature requirement for the system meant that hexanitrostilbene (HNS) was the choice for explosive.
Due to the high-temperature requirements of the job all the explosives, including shaped charges, detonation cord, boosters, time-delay units and the ballistic transfer device were all batch qualified for use at 470°F.
Specific explosives testing included ampoule testing:
Used to create batch-specific time-temperature curve.
Combined with multiple shaped charge tests at well conditions for final verification.
Ampoules containing HE sample 1 & 2
Notes: Ampule testing: monitors gas evolved when sample is held at a given temperature for a given length of time, 1 gram sample is sealed in a glass ampule, times can be greater than 1000 hours,
temperatures above 500 F, thermal stability test that most closely mimics the conditions that explosives are exposed to in oil-field operations

## Slide 9: Individual Component Testing and Certification
During the development and the pre-job preparation of this project, the company worked with many third-party vendors to carry out a full range of individual component tests. These tests were based on initial findings from up-front modeling. In addition, the company had many of these tests witnessed for verification purposes.
Tandem sub connectors
Firing head components
Gun system & components
Many items were included in the design verification phase of the project with everything else being certified through the quality plan.

## Slide 10: System Qualification
Many tests were completed during the system qualification phase of the project:
Gun system first article of machined gun bodies. (both pressure and temperature)
Ballistic survivability tests done on qualified gun bodies.
Post detonation gun drift test. (3.625”)
Shaped charges test fired after temperature soak.
Explosives time delay and transfer blocks functioned after temperature soak.
Detonating cord and booster test fired after temperature soak to ensure ballistic transfer.
Time-Temperature graph for explosives testing
Notes: Gun system first article of machined gun bodies. (both pressure and temperature)
Ballistic survivability tests done on qualified gun bodies.
Post detonation gun drift not to be more than 3.625”
Shaped charges test fired after temperature soak.
Explosives time delay and transfer blocks functioned after temperature soak to confirm time delay accuracy at temperature
Detonating cord and booster test fired after temperature soak to ensure ballistic transfer.

## Slide 11: System integrity Test, SIT
This was the final test performed to qualify the system for use as per the customer specified well conditions.
All items used in the test were from the same batches that were previously qualified for use in the well.
A 34,500-psi rupture disc was used in the firing heads. The entire assembly was lowered into the pressure vessel, and the vessel was then sealed. Temperature and pressure were then increased in a linear ramp from 72° F to 470° F (Approx. 11F every hour) and 0 to 28,000 psi, respectively over a period of 38 hours as this would mimic the temperature and pressure increase of running in hole.
2 x Guns with witness plate to confirm high order detonation and transfer
Redundant firing head system
34,500psi rupture discs
The system was then function at 34,000psi, with a good indication of detonation after 4 minutes 28 seconds.
Witness plate from test above, showing high-order detonation of the detonating cord

## Slide 12: System integrity Test, SIT
Time – Temperature data for the duration of the test
Notes: Red plot shows the 1st temperature sensor, Orange plot shows the 2nd temperature sensor, blue plot shows the pressure. This is to mimic what the system would see while running in hole and then while correlating on depth prior to firing. Pressure and temperature let off as soon as confirmation of detonation.

## Slide 13: Quality Plan
Other than the testing that was conducted on the component parts and the complete system integrity test, the quality plan is one of the fundamental elements that made this project delivery possible.
The quality plan was written by the company's quality assurance manager, who was fully integrated with the ballistics engineering group and who also had direct line of sight to the TCP product line team, enabling all parties to work together to streamline the process.
Hardware:
Pressure qualification of finished gun lot
100% hardness testing
100% seal bore surface finish inspection
20% ultrasound gun scallop thickness
100% scallop and phasing dimensional inspection
100% OD, length, ID drift, thread, seal bore
Third-party Components:
Velocity testing of detonating cord
Booster transfer tests
Manufacture date less than two years
Time delay transfer test lot
Transfer block tests lot
X-ray time delays lot
X-ray detonating cord
X-ray boosters
Shaped Charges:
QC production lot acceptance testing
Increased inspection rate
Built to order
Booster sensitivity to test shots (Gap test between detonating cord and shaped charge)

## Slide 14: Field Run Summary
 | System Ratings
Firing Pressure | 34,500
Temp | 470F
Fluid Compatibility | 19 PPG, 50% solids
Gun System | 3-1/2”-6SPF rock optimized charge (89 mm)
Clean-up | 1500 psi dymamic underbalance
Conveyance | Shoot and pull on drill pipe

## Slide 15: Conclusion
In conclusion it is without question a challenge for any organization to develop a technology that is required for such extreme conditions. However, with the correct team in place, combined with a full understanding of the customers requirements, these products can be delivered successfully on time for any project.
Work closely with all parties from the start of the project.
Use more than one independent test facility.
Be in control, do not accept any additional risk for a project.
As a customer be involved from the start, its your well! Make sure everything works.
Notes: Work closely with all parties from the start of the project and get to know and trust the other people
Use more than one independent test facility to check all results
Be in control, do not accept any additional risk for a project, maintain time lines and do not deviate from the plan
As a customer be involved from the start, its your well! Make sure everything works. Its in the customers hands to trust the supplier.

## Slide 16
Acknowledgements / Thank You
International Perforating Symposium
Slide 16

## Slide 17
Questions ?
Slide 17