## Slide 1: Perforating Weak Sands—A Review of Techniques
Andy Martin &
Kamaljeet Singh
IPS-15-24

## Slide 2: Agenda
* Mark of Schlumberger
Geomechanics
Sand Prediction Model
Practical Case
Summary
References

## Slide 3: A Little Bit of Geomechanics

## Slide 4: Weak and unconsolidated rocks
What is the range of strengths of very weak and weak rocks?
Zero strength Very very weak Very weak Weak
Dry sand Damp sand Weakly-cemented Stronger cement
high F lower F

## Slide 5: Failure Mechanisms—Shear
Shear failure (2)
  Compressive stress causes failure of single perforation tunnel
  Stress between perforations can cause a failure at the sand face, between perforations
Shear failure is the primary mechanism for sanding

## Slide 6: Failure Mechanisms—Tensile
Tensile failure (1)
  Force of flow erodes tunnel surface
  Common in very weak rocks or high flow rates
  Sand production may start upon initial inflow, with depletion, after shut-ins, or with water break-through

## Slide 7: What Influences Shear Failure?
Parameters we cannot influence
  Earth stresses
  Rock strength
Parameters we can influence
  Where to perforate (select stronger rock)
  Direction of perforations (most stable)
  Shaped charge type (tunnel diameter, penetration)
  Shot density and phase (perf-to-perf spacing)
  Clean perforations (reduce stress)
  Drawdown (reduce stress)
  Well startup (reduce stress)
  Water (avoid, monitor and shut off)
  Depletion (pressure support)

## Slide 8: What Influences Tensile Failure?
Parameters we can influence
  Drawdown
    Total flow rate
    Flow per perforation
    Sand production to surface
  Shot density
    Flow rate per perforation
Some opposing influences
  Increase shot density
  Increase perf-to-perf spacing

## Slide 9: Sand Prediction Models

## Slide 10: Sand Prediction Model
Rocks under axial flow
Sand separation
Transport mechanisms
Displacements of walls
2 to 21 Mpa UCS rocks
Wide range of sand separation mechanisms
Compare to modelled response of the perf tunnels - FE and semi-analytic

## Slide 11: Perforation Stability Modelling
3-D elastic stress analysis, fluid flow term, apparent strength
Data
  log-data, grain size
  perforation size, orientation
  insitu stresses, depletion
Engineering tool
  Geomechanics
Model validation (section 4 test)
North
s
h
s
v
s
H
s
z
s
q
s
r
s
r
s
z
s
q
Wellbore
Perforation
Tunnel

## Slide 12: Sand production - Stability Envelope
Reservoir Pressure (psi)
Safe
Drawdown
Failure
N O
F L O W
Critical Reservoir Pressure
O I L
+
S A N D
O I L
Wellbore
Pressure
(psi)

## Slide 13: Sand Prevention with Oriented Perforating
-5
-3
-1
1
3
5
Borehole Stresses
Damage occurs at stress concentrations
-5
-3
-1
1
3
5
1
3
5
MAX
Stress
MIN
Stress
1
3
5
MAX
Stress
MIN
Stress
-1
-3
(In this case, assume vertical well, σV > σH> σh)
Damaged rock
Min.
stress
Good
perforations
Max.
stress
High stress concentration
Perforation in intermediate direction is generally worst

## Slide 14: Sanding Sensitivities – Perforation Diameter
Decreasing Perforation Diameter
Normalized hole size

## Slide 15: Sanding Sensitivities – Perforation Orientation

## Slide 16: Sanding Sensitivities – Stress Anisotropy & UCS
Maximum horizontal stress
Increasing SHmax
Rock Strength
Increasing UCS

## Slide 17: Optimum Phasing
Maximize perf.-to-perf spacing for a given spf and phasing

## Slide 18
Block Tests—Orientation Effects
Multiple Perforations in Sandstone shot at 400 psi U/B
Downside perforation
Topside perforation

## Slide 19
Bent Wellbore Setup

## Slide 20: Optimized Perforating
Perforation selection from model
  Orient to minimize stress contrast
  Decrease perforation hole size – Appropriate Charges
  Perforate strongest zones (selective perforations)
  Optimize perforation to increase perforation spacing (> 4 hole diameter)

## Slide 21: Practical Case

## Slide 22
Oriented Perforating North Sea Well

## Slide 23: Sand Detection Log North Sea Well

## Slide 24: North Sea Existing Wells
Existing perforation in deviated wells
  3 3/8” 5 spf, +/-10 to top
  2 7/8” 6 spf, +/-10 to top
Increase spf by shooting low side in same directions
Doubling spf would reduce drawdown, reduce erosional flow and limit sanding risk

## Slide 25: Zones Producing Sand
Double shoot or:
Extreme shot density guns with small DP shaped charges
  Small holes more stable
  Reduce pressure drop
  Reduce flow rate per perforation

## Slide 26: Summary
Understand the Geomechanics
Shoot in the most stable directions
Respect perf-to-perf spacing
Maximize shot density
Don’t be afraid to reperforate or use extreme spf
Shut off water

## Slide 27: Some References
OTC 19130 Oriented Perforating as a Sand Prevention Measure
SPE 47360 Benefits of Assessing Solids Production Risk in a North Sea Reservoir Using Elastoplastics Modelling
SPE 50387 Experimental Investigation of Sanding Propensity for the Andrew Completion
SPE 57954 Oriented Perforating for Sand Prevention
SPE 58788 Perforating Requirements for Sand Prevention
SPE 93639 High-Accuracy Oriented Perforating Extends the Sand-Free Production of the Andrew Field
SPE 102242 Bokor—A New Look at Sand Production in a Mature Field
SPE 107785 Optimized Perforation Tunnel Geometry, Density and Orientation to Control Sand Production

## Slide 28: Perforating
* Mark of Schlumberger
Questions?
Geomechanics
Sand Prediction Model
Practical Case