## Slide 1: 2015 International Perforating Symposium The Renaissance Hotel, Amsterdam May 19 – 21, 2015
Fast-physics Computational Model to Predict Complex Transient Dynamics of API Section IV Lab Tests
Derek Bale, Rajani Satti, Minsuk Ji, Baker Hughes
IPS –15-5

## Slide 2: Overview of the Presentation
Introduction
Perforation flow laboratory
Existing laboratory event modeling
Objectives
Our design philosophy
Fast-physics: Model and results
Fast-physics: Plans for future
Conclusions
IPS – 15-5

## Slide 3: Introduction
Next-generation well completions
      High-pressure/high-temperature
      Ultra-deepwater
      Long horizontals
Understanding the transient fluid dynamics during the
perforating process is critical to perforating well design.
Transient dynamics influenced by
job design parameters:
      Gun design
      Formation properties
      Under/Overbalance conditions
IPS-15-5
Notes: As the industry looks forward to next—generation well completions (HPHT, Deepwater, Long horizontals), perforating job design plays a critical role is these challenging scenarios. In particular, given the small time scales (few milliseconds) involved in perforating, it is of utmost importance to properly understand the transient fluid dynamics that occurs as a result of the interaction between the wellbore, gun system and the formation. Job design parameters such as gun design and specifications, formation properties (like porosity, permeability, UCS), and wellbore conditions (overbalance, static underbalance, dynamic underbalance) ultimately effect the transient dynamics.

## Slide 4: Perforation Flow Laboratory
Flow laboratory: Clear vehicle to study and understand the coupled effects between transient dynamics and job design parameters.
Measurements from a Section-IV test:
    Pre- and post-flow permeability
    Core flow efficiency
    Productivity
    Dynamic high-speed pressure
    Perforation tunnel characteristics
    Clean-up and underbalance optimization
IPS –15-5
Notes: A clear vehicle to study and understand such dependencies (transient dynamics vs job design parameters) is the API-RP 19B Section IV test in which a single shape charge is used to perforate a rock core, and subsequent core flow can be measured and characterized using high-speed pressure gauges and flow meters.

## Slide 5: Perforation Flow Laboratory
High-Speed Gauge Data
wellbore
reservoir
The dynamic pressure data provides insight into the perforation process.
Though the details of the pressure curve look complicated, the general trends of the dynamics are dominated by only a few physical processes.
Challenges:
    Experimental costs
    Limited data
    Impractical when DOEs are required
IPS –15-5
Wellbore Pressure (psi)
Notes: The generation and flow characteristics of the perforation tunnel strongly depend on the features of the pressure curve shown (e.g., minimum pressure, temporal gradients, etc.). Note the extremely small time scale (<1sec) that characterizes the post-perforating event.
Though the details of the pressure curve look complicated, the general trends of the dynamics are dominated by only a few physical processes that can be mathematically simplified and modeled.
Challenges:
- Experimental costs
- Limited data
- Impractical when large DOEs (design through experimental studies) are required

## Slide 6: Laboratory Event Modeling
Pressure (PSI)
Time (s)
High-Speed Gauge Data
wellbore
reservoir
Simulation (wellbore)
Simulation (reservoir)
Existing models:
  Limitations in representing flow lab geometry
  Too many “free parameters” unrelated to the flow physics
  A decent fit requires multiple ~30 min. runs for tuning
IPS –15-5
Laboratory simulator:
  Useful tool to aid in experimental data analysis and interpretation
  Helps in planning and optimizing experiments
  Can reduce the size of meaningful DOEs (saves $$$)
  Modeling can be upscaled to field-scale analysis (improves perforating jobs)

## Slide 7: Objectives of the Study
Understand and analyze the complex transient dynamics obtained from an API Section-IV experiment.
Develop one-of-its-kind fast computational model based on simplified dominant processes that play an important role during the Section-IV test.
Predict the complex pressure transients that are generated using a dynamic perforating event.
IPS –15-5

## Slide 8: Our Design Philosophy
IPS –15-5
Presented in IPS –15-19
Notes: We recently developed an engineering workflow that combines experimental and numerical modeling to evaluate and optimize the shaped charge performance. The workflow is primarily targeted towards exploiting the capabilities of a perforation flow laboratory in conjunction with numerical modeling. As seen from the workflow below, apart from the experimental testing in the flow laboratory, our modeling efforts are focused on two aspects:
Development of a novel full-physics CFD model that utilizes digital rock physics to simulate the flow around the true geometry of the perforation tunnel.
Development of a fast computational model based on laboratory apparatus to complement the transient effects seen in lab experiments (focus of this work)

## Slide 9: Fast Physics: Model Development
Conceptual
Simple shape of the pressure transients hint at two dominant physical processes
Test of time scales as rough estimators.
Full Numerical
Develop full models for gun, wellbore, and reservoir.
Implement them in a bench-top environment.
Fast Physics
Use full numerical simulation to understand dominant processes.
Recast full model into simplified “dominant physics” model.
Proof of Concept
Comparison of measured pressure transients with computed values.
IPS –15-5
We used four major development steps to create this simulation tool :
Notes: We used four major development steps to create this simulation tool

## Slide 10: Fast-Physics: Model Components
Wellbore
Gun chamber
Rock core
Connectivity to accumulators
Perforation tunnel
IPS –15-5
Notes: The schematic above shows the key components of the model (which is similar to the Section-IV apparatus) which include the wellbore, gun chamber, rock core, accumulators and connections and most importantly, the perforation tunnel. Appropriate numerical conditions relating to initial pressures in wellbore, pore, gun chamber are considered. The rock core properties considered include the porosity and permeability.

## Slide 11: Fast-Physics: Model Assumptions
Wellbore
  Weakly compressible
  Isothermal
  Inviscid flow
Gun Chamber
  Compressible ideal gas
  Gas expansion is adiabatic
  Initially at atmospheric pressure
Rock Core
  Uniform porous medium
  Linear Darcy flow
  Weakly compressible liquid (incompressible rock)
  Pore pressure greater than wellbore
IPS –15-5

## Slide 12: Fast-Physics: Preliminary Results
Model fit to measurement data is very good.
No parameter “fudging”, all parameters are physics-based and their values lend insight into the physical flow
Each run takes <100 ms to run  a fitting tool will be simple and feasible
Efficient tool to understand - underbalance conditions - overbalance conditions - influence of damage zones - clean up dynamics
IPS –15-5

## Slide 13: Fast-Physics: Preliminary Parametric Analysis
Gun | Wellbore | Rock Core
geometry (volume) | fluid properties (compressibility) | permeability (volume and non-uniformity)
gas constant | geometry (volume) | Porosity
external conditions | initial state (static underbalance) | Viscosity
shape charge characteristics |  | 
An example of modifying permeability
Notes: The table above again shows the dominant parameters that are used to represent the Section-IV test using a simplified, yet full-physics mathematical model.
The plot shows an example where the model can be quickly used to understand the influence of core permeability on the dynamics of the pressure curve. As expected, as permeability is increased from 50md to 200md,
- the magnitude of dynamic underbalance is reduced
- The time required to reach equilibrium is reduced with increasing permeability

## Slide 14: Fast-Physics: Future Plans
Preliminary fast-physics model
Model perforation tunnel geometry
Model damage zones
Burn models
Detailed validation using gauge/CFD data
Integrate clean-up model with fast-physics
Upscale results to existing
field-scale simulator
Fundamental investigation of perforation dynamics: CFD
CFD models: crushed zone, exact tunnel geometries
Notes: As for the roadmap going forward, the following are the key steps involved:
Current status: First-gen fast physics model to simulate transient dynamics of a Section-IV test has been developed
Improve the model by including perforation geometry effects, crushed zones and more importantly, relevant burn models
Comprehensive validation of the model using gauge data and CFD
Couple BHI’s proprietary clean-up model with fast physics to provide complete insight into underbalance and clean-up predictions
Upscale the fully validated results from fast physics model to field scale simulator since both of them share the same benchtop platform (similar fundamental physics)
It should also be noted that in order to complement and support the development of the fast physics model, we plan to leverage CFD tools. CFD will be used to investigate fundamental mechanisms of perforation dynamics, validations and other critical predictive correlations (influence crushed zone and exact tunnel shape and size). As an example, the animation above shows how we are taking a fundamental approach in understanding perf dynamics. A basic nozzle flow is considered with water at the inlet and quiescent air filled in the channel. The animation (two phase flow) shows how pressure gradients drive the water column and compress the air in the closed channel system. We intend to use these numerical methods to develop a wellbore-gun-core model using CFD where the fluid dynamics is primarily driven by pressure gradients in a two-phase flow system. It should be noted that CFD will be used for subsequent validation of our fast-physics model. Although CFD is a valuable tool, expensive run times are a constraint in fully deploying CFD for dynamic perf studies.

## Slide 15: Conclusions
A new model and simulation tool has been developed for interpretation of the pressure transients of an API-RP 19B Section IV flow test.
  Model is based on simplified dominant physics
  Each simulation runs in < 1 second
  Its simple form enables interpretation based directly on physical parameters.
Preliminary results show good agreement between measured high-speed data and computed dynamic pressure data.
As part of our future plans, we are working on
Extending the fast-physics to include details effects of perforation
tunnel characteristics (true size/shape and crushed zone)
Comprehensive validation using gauge and CFD data
Incorporate clean-up and upscaling models

## Slide 16
Acknowledgements / Thank You
Committee of the 2015 IPS Europe
Slide 16
IPS – 15 - 5

## Slide 17
Questions ?
Slide 17
IPS – 15 - 5